## Slide 1: Final Year Project Seminar Machine Learning for Defect Detection in 3D Printing Process
Boon Ho
Supervisor: Dr. Paul Hooper

## Slide 2: Background
1. 3D Printing/ Additive manufacturing, AM
  Manufacturing technique which manufactures a product in a layer wise additive manner.
  Advantages: Unprecedented design freedom and less material wastage
2. Laser Powder Bed Fusion, LPBF
  Laser scans in a predefined path on a platform with uniformly spread metallic powder.
  Creates a localised region below the laser beam known as melt pool.
  Actively melts and fuses the metallic powder.
Laser Beam
Powder
Melt pool
Scan Direction
Figure 1 LPBF printing process

## Slide 3: Background
3. Defects Formation
  There will always be defects in the product. Some defects are tolerable, some are not.
  Optimising scan parameters alone is insufficient – In-situ monitoring.
  Melt pool dynamics is related to defects formation.
  Eg. Denuded zone forms when the surface tension of the melt flow
  entrains nearby particles into the melt flow. Partially melted particles
  then ejected as spatter particles.
1. S.A. Khairallah et al. , Laser powder-bed fusion additive manufacturing: Physics of complex melt ﬂow and formation mechanisms of pores, spatter, and denudation zones, Acta Materialia 108 (2016) 36–45
Figure 2: [1] Melt pool regions and denudation

## Slide 4: Objectives
  The project focuses extensively on analysing the melt pool dynamics through the lens of machine learning models. The main objectives are:
Explore different machine learning models capable of detecting and classifying anomalous melt pools under different scans.
Evaluate the machine learning models performance with multiple test data.

## Slide 5: Datasets
  Coaxial LPBF monitoring system which resolves the temperature field of the melt pool both in time and space
  Video frames of resolved melt pools
  Positional Dataset: x and y coordinates of the scan path
Melt pool video frame (128 x 128)
Positional Dataset

## Slide 6: Exploratory Data Analysis
Metrics for visualisation
  Standard Deviation: SD
  Proportion of Bright Pixels: PBP
  Subregion Mean: SRM
Figure 4: Standardised Metrics against melt pools’ frame ID.
Block 4 focus height = 4 mm
Block 6 focus height = 0 mm
Block 4
Block 6
(a)
(b)
(c)
Figure 3: (a) Tail Separation (b) Plume (c) Spattering

## Slide 7: Region Props Features Extraction
Python’s Skimage Region Props function for features extraction:
Region Props Features
  1. Melt pool
  Size
  Eccentricity
  2. Spatter particle
  Quantity
  Average size
  Average eccentricity

## Slide 8: Features Extraction
Average spatter area
Melt pool size
Block 4
Block 6
Block 4
Block 6

## Slide 9: Machine Learning Frameworks

## Slide 10: One Class Learning Framework
  Unsupervised method of training machine learning classifiers when some classes in the dataset are either present in a small amount, or have no well-defined characteristics.
  One class classifiers are models which specialised in recognising the normal instances.
  Anomalous melt pools are not necessarily the minorities, but they are not very well-characterised.
  Eg. How many spatter particles a melt pool must eject and how big must they be for the melt pool to be considered as an anomalous instance?
  Deep convolutional autoencoder used as one class classifier.

## Slide 11: Autoencoder: Introduction
General architecture of an autoencoder.
Latent vector
(Bottleneck)
  Dimensionality of the latent vector is a design choice. In this project, specified as 2D.
  Want X to be similar to X’.
  Loss Function: Euclidean distance between both images.
(Input Image)
(Output Image)

## Slide 12: Data Pre-sieving
  Constraint: Training dataset must contain mostly normal melt pool images.
  For convenience, label melt pool frames as follow
  Standardise the features and apply K-means Clustering and analyse the proportion of melt pool images in each cluster.
Focused | Out-of-focus
Focus height = 0, +4mm | Focus height = -4mm, +8mm
Build 2 Data
Build 3 Data
“focused” melt pool images ( ) as training data.
Table 1: Labelling of the dataset

## Slide 13: Clusters Analysis
Average Spatter
Area
Average Spatter
Eccentricity
Number of spatter particles
Melt Pool
Blob Area
Melt Pool Eccentricity
Take the centroid coordinates of the clusters and show them in bar plots.
Zero spatter properties
Similar melt pool properties

## Slide 14: Autoencoder: Testing
Small Reconstruction error

## Slide 15: Autoencoder: Testing
Large Reconstruction error

## Slide 16
Training Data
Testing Data
Training Data
Testing Data

## Slide 17: DBSCAN
  Further cleaning with density based clustering algorithm, DBSCAN:

## Slide 18: Performance Evaluation
  Manually labelled 1500 datapoints for validation and testing. Classify the data into “Normal” and “Anomalous”.
Autoencoder
Autoencoder trained on DBSCAN

## Slide 19: Performance Evaluation
 | Categories | Avg. Recall | Avg. Precision
K-Means Clustering | Normal | 0.89 | 0.54
 | Anomalous | 0.29 | 0.73
Autoencoder without DBSCAN | Normal | 0.71 | 0.96
 | Anomalous | 0.75 | 0.60
Autoencoder with DBSCAN | Normal | 0.76 | 0.96
 | Anomalous | 0.76 | 0.71
Autoencoder > K-Means
Autoencoder slightly improve its performance with DBSCAN

## Slide 20: Automated Features Extraction Framework
  Motivated by the data compression capability of the autoencoder.
  But the latent space of an autoencoder is not smooth (highly packed in one region). Possible to address this with a probabilistic variant of an autoencoder, variational autoencoder (VAE).
  The distributions of melt pool geometries -> smoother latent encodings.

## Slide 21: Disentangled Variational Autoencoder
  Loss function:
Probabilistic Encoder,
Probabilistic Decoder,
µ
σ
Similarity metric
KL Divergence
Similarity metric is conceptually the same as autoencoder’s loss function
KL Divergence term ensures that the VAE learns the distribution of the latent components instead of just a point encoding in the latent space
is the relative weightage of the KL Divergence term

## Slide 22: Image Cropping
Centroid
Expand 16 px in each direction
Expand 16 px in each direction
Results in 32x32 cropped image

## Slide 23: Disentangled Variational Autoencoder
  Specified the latent dimension as 3D for easy visualisation.
  Specified a range for each latent components and pass it to the probabilistic decoder to inspect the melt pool representations captured.
  Show the generated images in grid view.

## Slide 24
Tail Length & Direction (Z3)
Size (Z1)
Roundness (Z2)
Size (Z1)

## Slide 25: Automated Features Extraction Framework
Z1
Z2
Z3
(a)
(b)
(c)
The distributions of latent components (a) Z1, (b) Z2 and (c) Z3.
Meander scanning, hence makes sense to be bimodal.
Z1: Size, Z2: Roundness, Z3: Direction and tail length

## Slide 26: Anomalies Detection and Classification
Z1
Z2
Z3
K-Means Clustering fitted on training data then deploy for testing
Number of clusters specified as two. Makes sense to compare melt pools heading in the same direction.
Euclidean distance from the clusters centroid as anomaly metric.

## Slide 27: Anomalies Classification
  Three supervised classifiers were trained: Random forest (RF), support vector machine(SVM) and k-nearest neighbours (KNN).
  Classification performance: (The recall metric generally ranges in between 70% to 80%)
Confusion Matrix for Build 2 data classifications results. Focus height = +4mm (a)SVM, (b)KNN and (c)RF.

## Slide 28
Confusion Matrix for Build 3 data classifications results. Focus height = 0mm (a)SVM, (b)KNN and (c)RF.
(a)
(b)
(c)
(a)
(b)
(c)
Confusion Matrix for Build 2 data classifications results. Focus height = -4mm (a)SVM, (b)KNN and (c)RF.

## Slide 29
Build 2 Correct Classifications (a) Unstable Tail, (b) Plume and (c) Large melt pools.
(a)
(b)
(c)
Build 3 correct classifications. (a) Long, (b) Large, (c) Unstable tail and (d) Plume.
(a)
(b)
(c)
(d)

## Slide 30: Case Study: Relating Melt Pool Anomalies to Defects
  Overlay the positional data on a microscopic image of a
  printed rectangular block.
  Aim: Inspect anomaly metrics at various locations of defects.
  Developed an interactive tool for inspection.
  Caveat: Dark patches shown could be the shadowing effects and not
  actual defects.
(a)
(b)
(a) Positional data overlaid on microscopic image (b) Original microscopic image

## Slide 31
1
3
7
10
Variation of averaged anomaly metrics within the specified radius.

## Slide 32
1st Selection:
Plume
3rd Selection:
Plume

## Slide 33
7th Selection:
Unstable Tail
10th Selection:
Unstable Tail

## Slide 34
3
7
10
Variation of averaged anomaly metrics within the specified radius.

## Slide 35: Conclusion
  Proposed two frameworks for melt pool anomalies detection and classification:
  One class learning with deep convolutional autoencoder (Metric: Reconstruction error)
  Disentangled Variational Autoencoder for automatic features extraction (Metric: Distance from respective centroids)
  Classifications: Unstable tail, Large Melt Pools, Plume, Long Melt Pools
  Future work will include more variations of melt pools for the training of disentangled VAE.

## Slide 36
The End